## Slide 1: Cortex-M4 Efficient, easy to use digital signal control
Terry FAE
ARM Korea

## Slide 2: Microcontrollers address broad markets
Human interfaces
EPOS terminals
Image processing
Audio interfaces
Power management
UPS
Lighting systems
AC/DC converters
Automotive
ABS systems
Chassis control
Airbag systems
Industrial Applications
Appliances
Lighting
Motion control
Medical instrumentation
Blood pressure meters
Glucose meters
Defibrillators
Connectivity
Bluetooth
Zigbee
Ethernet
Smart Metering
Gas and water
Electricity
Connectivity
Motor control
Field oriented control
Stepper motors
BLDC motors etc
Audio
MP3 players
Wireless headsets
Virtual surround
Notes: The MCU markets are very wide
You need a variety of devices to address these markets
The M0 and M3 already address a lot of them ..
And the underlying requirement for the future is some level of signal processing

## Slide 3: Why another Cortex-M processor?
Address new markets requiring digital signal control
  Digital Signal(Processor + Micro)Controller
  An intelligent blend of MCU and DSP features demanded
    Upper limits of bandwidth challenged in general purpose MCUs
    Hard to learn/program technology in many general purpose DSPs
Extend the Cortex-M portfolio to cover new markets
  Cortex-M0 for mixed signal devices and state machine replacements
  Cortex-M3 for mainstream 32-bit microcontrollers
  Opportunity - high end MCUs and DSC market
Introduce ARM strengths to digital signal control market
  Very high energy efficiency – more processing in less mW
  Strong software ecosystem – easy to program and use

## Slide 4: Cortex-M4 - What’s unique about it?
Most energy efficient 32-bit
embedded processor for
digital signal controllers
Brings high performance signal
processing within the reach of the
typical MCU programmer
Notes: Most MCUs are not as energy efficient as M4 for signal processing algorithms , Most DSPs are not as easy to program as M4
M4 provides the best balance

## Slide 5: Cortex-M4 for digital signal control
Cortex-M4
MCU
Ease of use
C Programming
Interrupt handling
Ultra low power
DSP
Harvard architecture
Single cycle MAC
Floating Point
Barrel shifter
Notes: Best of both worlds ….

## Slide 6: Cortex-M processors binary compatible
Notes: Complete upwards binary compatibility

## Slide 7: Cortex-M4 SIMD instructions
SIMD extensions perform multiple operations in one cycle Sum = Sum + (A x C) + (B x D)
SIMD techniques operate with packed data
  Algorithm developers can also reduce memory load instructions
32-bit
32-bit
64-bit
64-bit

## Slide 8: Cortex-M4 extended single cycle MAC
OPERATION | INSTRUCTIONS
16 x 16 = 32 | SMULBB, SMULBT, SMULTB, SMULTT
16 x 16 + 32 = 32 | SMLABB, SMLABT, SMLATB, SMLATT
16 x 16 + 64 = 64 | SMLALBB, SMLALBT, SMLALTB, SMLALTT
16 x 32 = 32 | SMULWB, SMULWT
(16 x 32) + 32 = 32 | SMLAWB, SMLAWT
(16 x 16) ± (16 x 16) = 32 | SMUAD, SMUADX, SMUSD, SMUSDX
(16 x 16) ± (16 x 16) + 32 = 32 | SMLAD, SMLADX, SMLSD, SMLSDX
(16 x 16) ± (16 x 16) + 64 = 64 | SMLALD, SMLALDX, SMLSLD, SMLSLDX
32 x 32 = 32 | MUL
32 ± (32 x 32) = 32 | MLA, MLS
32 x 32 = 64 | SMULL, UMULL
(32 x 32) + 64 = 64 | SMLAL, UMLAL
(32 x 32) + 32 + 32 = 64 | UMAAL
32 ± (32 x 32) = 32 (upper) | SMMLA, SMMLAR, SMMLS, SMMLSR
(32 x 32) = 32 (upper) | SMMUL, SMMULR
All the above operations are single cycle on the Cortex-M4 processor

## Slide 9: Cortex-M4 8,16-bit SIMD arithmetic
 | S Signed | Q Signed Saturating | SH Signed Halving | U Unsigned | UQ Unsigned Saturating | UH Unsigned Halving
ADD8 | SADD8 | QADD8 | SHADD8 | USADD8 | UQADD8 | UHADD8
SUB8 | SSUB8 | QSUB8 | SHSUB8 | USUB8 | UQSUB8 | UHSUB8
ADD16 | SADD16 | QADD16 | SHADD16 | UADD16 | UQADD16 | UHADD16
SUB16 | SSUB16 | QSUB16 | SHSUB16 | USUB16 | UQSUB16 | UHSUB16
ASX | SASX | QASX | SHASX | UASX | UQASX | UHASX
SAX | SSAX | QSAX | SHSAX | USAX | UQSAX | UHSAX
USAD8 | Unsigned Sum of Absolute Difference (8 bits) |  |  |  |  | 
USADA8 | Unsigned Sum of Absolute Difference and Accumulate (8 bits) |  |  |  |  | 
Prefix
ASX
1. Exchanges halfwords of the second operand register
2. Adds top halfwords and subtracts bottom halfwords
Instr
SAX
1. Exchanges halfwords of the second operand register
2. Subtracts top halfwords and adds bottom halfwords

## Slide 10: Cortex-M4 single precision floating point
IEEE 754 standard compliant
Decoupled floating point pipeline
Single-precision floating point math
  Add, subtract, multiply, divide, MAC and square root
  Fused MAC – higher precision
OPERATION | CYCLE COUNT
Add/Subtract | 1
Divide | 14
Multiply | 1
Multiply Accumulate (MAC) | 3
Fused MAC | 3
Square Root | 14

## Slide 11: Highest in-class efficiency
Chart: 
| IIR | FFT
16-bit Renesas SH-2A | 1 | 1
Cortex-M4 | 0.41011 | 0.59759
Chart: 
| IIR | FIR | FFT
16-bit Renesas SH-2A | 1 | 1 | 1
Cortex-M4 | 0.58539 | 0.69066 | 0.50377
Cycle counts on DSP tasks compared, smaller is better
16-bit MCU
32-bit MCU
32-bit Cortex-M4
The Cortex-M4 is ~2X more efficient on most DSP tasks than
leading 16 and 32 bit MCU devices with DSP extensions
Notes: M4 can do these tasks in less than half the cycles than competitive devices.. Leaves room to do much more in a flash limited MHz bandwidth and also keeps power down

## Slide 12: Nested Vectored Interrupt Controller
Faster interrupt response
  With less software effort
ISR written directly in C
  Interrupt table is simply a set of pointers to C routines
  ISRs are standard C functions
Integrated NVIC handles:
  Saving corruptible registers
  Exception prioritization
  Exception nesting
8051 | Cortex-M
SJMP/L JMP from vector table to handler PUSH PSW ORL PSW, #00001000b (to switch register bank) Starting real handler code | Starting real handler code
Tail-chain

## Slide 13: Cortex-M4 low power implementation
Cortex-M4 features architected support for sleep states
  Enables ultra low-power standby operation
  Critical for extended life battery based applications
  Includes very low gate count Wake-Up Interrupt Controller (WIC)
NVIC
Cortex-M4
WIC
Wake-up
External interrupts
Wake-up
sensitive
Interrupts
Power Management Unit
Deep
Sleep
Sleep
  CPU can be clock gated
  NVIC remains sensitive to interrupts
Deep sleep
  WIC remains sensitive to selected interrupts
  CPU/NVIC clock gated or in state retention
WIC signals wake-up to PMU
  Cortex-M4 can be woken almost instantaneously
  React to critical external events

## Slide 14: Wake-up interrupt controller (WIC)
Maximum power-down with minimum user intervention

## Slide 15: Summary
What has just been announced?
  Product – Cortex-M4 , Product category - Digital Signal Control
  Key features – Single cycle MAC, Floating point unit
  Key markets - Motor control, industrial automation, automotive, audio
Why this processor ?
  Most high-end MCUs need some level of DSP capabilities
  An efficient blend of control and DSP features is very attractive
Who has licensed it ?
  6 of the top MCU companies have licensed the Cortex-M4.
How is it different ?
  Most efficient 32-bit DSC processor in the market
  Easy to use tools through extremely strong software ecosystem

## Slide 16: Cortex-M4 processor Next Cortex-M family member driving further standardization

## Slide 17: Cortex Microcontroller Standard (CMSIS)
Abstraction layer for all Cortex-M processor based devices
    CMSIS-CORE : API for Cortex-M processor and core peripherals
    CMSIS-DSP : DSP Library with 61 functions for Cortex-M
    CMSIS-SVD : XML system view description for peripherals
    CMSIS-RTOS : API for RTOS integration
Benefits to the embedded developer
  Consistent software interfaces for silicon and middleware vendors
  Simplifies re-use across Cortex-M processor-based devices
  Reduces learning curve, development costs, and time-to-market
New
Notes: 17
For the benefit of the embedded developer
- Reduce Complexity
- Provide Industry-Wide Programming Standards
- Support Partnerships and Innovation

## Slide 18: Cortex-M4 CMSIS extensions
Cortex-M4 support available today in MDK-ARM and ARM Compiler
  C Compiler intrinsic functions for Cortex-M4 extended Instructions
  Optimized Floating Point Library using FPU CPU Instructions
  Complete µVision Debugger support; including Instruction Set Simulation
CMSIS - Expanded with Cortex-M4 Features (Intrinsic Functions)
  Every CMSIS compliant C Compiler supports Cortex-M4 extensions
Optimized CMSIS DSP Library
  Designed to make DSP programs
  easy to develop for MCU users
  General Functions math, trigonometric, control functions (building blocks)
  Digital Filter Algorithms for filter design utilities and DSP toolkits (MathLab, LabVIEW, etc.)

## Slide 19: CMSIS-DSP Library
C Source Code, optimized for Cortex-M4
For CMSIS compliant C Compilers (ARM/Keil, IAR, GCC)

## Slide 20: CMSIS DSP Library Performance
Cortex-M4 SIMD + FPU
  Fix point: ~2x faster
  Floating point: ~10x faster
2,244
8,819
FIR q15 fixed point
41
IIR q31 fixed point
8,596
PID q15 fixed point
8,310
Matrix Mul fixed point
13,619
158,878
Correlationfloating point
2,462
27
2,462
DSP Library Benchmark: Cortex-M3 vs. Cortex-M4
Cortex-M3
Cortex-M4
Memory Access Cycles
Cycles: smaller numbers are better
- 75%
- 35%
- 69%
- 70%
- 91%

## Slide 21: ARM Connected Community

## Slide 22: Summary
What has just been announced?
  Product – Cortex-M4 , Product category - Digital Signal Control
  Key features – Single cycle MAC, Floating point unit
  Key markets - Motor control, industrial automation, automotive, audio
Why this processor ?
  Most high-end MCUs need some level of DSP capabilities
  An efficient blend of control and DSP features is very attractive
Who has licensed it ?
  6 of the top MCU companies have licensed the Cortex-M4.
How is it different ?
  Most efficient 32-bit DSC processor in the market
  Easy to use tools through extremely strong software ecosystem
780370