## Slide 1
High-performance Cortex™-M4 MCU
STM32 F4 series
Lloyd HYUN
ST Microelectronics MCU Technical FAE
April 2012

## Slide 2: Contents
STM32 series
Highlight
Performance Graph
ART Accelerator
Bus Matrix
Power Efficiency
Components
Portfolio
Tools & Software

## Slide 3
Binary and tool compatible
MCU
Cortex-M processors
Forget traditional 8/16/32-bit classifications
  Seamless architecture across all applications
  Every product optimised for ultra low power and ease of use
Cortex-M0
Cortex-M3
Cortex-M4
“8/16-bit” applications
“16/32-bit” applications
“32-bit/DSC” applications

## Slide 4: All STM32 Cortex™-M MCUs
32bit / DSC Applications
16bit / 32bit Applications
8bit /16bit Applications
High-Performance DSP MCUs
Cortex-M4 (168MHz)
Flash (up to 2MB)
SRAM (up to 256KB)
STM32 F4
STM32 F1
STM32 F2
Mainstream MCUs
Cortex-M3 (24~72MHz)
Flash (16KB~1MB)
SRAM (up to 96KB)
High-Performance MCUs
Cortex-M3 (120MHz)
Flash (256KB~1MB)
SRAM (up to 128KB)
STM32 F0
Cortex-M4
Cortex-M3
STM32 L1
Ultra-low-power MCUs
Cortex-M3 (32MHz)
Flash (32~384KB)
SRAM (up to 48KB)
Cortex-M0
Entry-level MCUs
Cortex-M0 (48MHz)
Flash (16~128KB)
SRAM (up to 20KB)

## Slide 5: 5 Product Series
8/16-bit applications

## Slide 6: STM32 Genealogy and Growth
Chart: 
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012
Série 1 | 0 | 9 | 33 | 127 | 205 | 246
32bit / DSC（Cortex-M4）
16bit / 32bit（Cortex-M3）
8bit / 16bit（Cortex-M0）
Mainstream MCUs
STM32F1
Connectivity
High-Performance MCUs
STM32 F2
STM32F1
Value
STM32 Sales Trend
STM32 F1
STM32 F4
High Performance DSP MCUs
x 3.7
x 3.8
x1.6
Enhancing Portfolio and Growing Steadily Since 2007
STM32 L1
Ultra-low-power MCUs
STM32 F0
Entry-level MCUs

## Slide 7: STM32 Manufacturing Commitment
Fab 4
Fab 1
Fab 3
Fab 2
Notes: These are locations where we do double sourcing front end. They work by pairs for our MCUs.
Fab 4 and 3 together and Fab 1 and 2 together

## Slide 8: STM32 F4 Series highlights 1/4
ST is introducing STM32 products based on Cortex M4 core. Over 30 new part numbers pin-to-pin and software compatible with existing STM32 F2 Series.
The new DSP and FPU instructions combined to 168Mhz performance open the door to a new level of Digital Signal Controller applications and faster development time.
STM32 Releasing your creativity

## Slide 9: STM32 F4 Series highlights 2/4
Advanced technology and process from ST:
Memory accelerator: ART Accelerator™
Multi AHB Bus Matrix
90nm process
Outstanding results:
210DMIPS at 168Mhz.
Execution from Flash equivalent to 0-wait state performance up to 168Mhz thanks to ST ART Accelerator

## Slide 10: STM32 F4 Series highlights 3/4
More Memory
Up to 1MB Flash,
192kB SRAM: 128kB on bus matrix + 64kB on data bus dedicated to the CPU usage
Advanced peripherals shared with STM32 F2 Series
USB OTG High speed 480Mbit/s
Ethernet MAC 10/100 with IEEE1588
PWM High speed timers: Now 168Mhz max frequency!
Crypo/hash processor, 32-bit random number generator (RNG)

## Slide 11: STM32 F4 Series highlights 4/4
Further improvements
Low voltage: 1.8V to 3.6V VDD , down to 1.7*V on most packages
Full duplex I2S peripherals
12-bit ADC: 0.41µs conversion/2.4Msps (7.2Msps in interleaved mode)
High speed USART up to 10.5Mbits/s
High speed SPI up to 37.5Mbits/s
Camera interface up to 54MBytes/s
*external reset circuitry required to support 1.7V

## Slide 12
STM32 F4: World’s #1 in performance
It takes ART to be #1 in performance: It is a combination of core, embedded Flash design, process, acceleration techniques.
Dhrystone

## Slide 13: STM32F4 versus competitors (Coremark)
Notes: uPDATE

## Slide 14: ST’s ART Accelerator™
The adaptive real-time memory accelerator unleashes the Cortex-M4 core’s
maximum processing performance equivalent to 0-wait state execution
Flash up to 168 MHz
Notes: The ART Accelerator is an ST technology using a prefetch queue and branch cache technology to access 128-bit wide Flash. Based on CoreMark benchmark, the result is a performance equivalent to 0-wait state execution from Flash.
The branch cache is made of 64 × 128-bit buffers for code and 8 x 128-bit buffers for data. Each time an event such as subroutine call, an interrupt or a branch occurs and breaks the linear execution of the code, the ART Accelerator checks if the first instructions of the event are already stored in the cache, and if so, the instruction is immediately pushed to the prefetch queue with no performance loss. The prefetch cache is so deep that most applications achieve a 0-wait state execution performance from Flash.

## Slide 15: System Architecture – Flash performance
15

## Slide 16: System Architecture – Flash performance
16

## Slide 17: System Architecture – Role of the ART accelerator 1/2
17

## Slide 18: System Architecture – Flash performance
18

## Slide 19: System Architecture – Role of the ART accelerator 2/2
19

## Slide 20
32-bit multi-AHB bus matrix
Real-time performance
Compressed audio stream (MP3) to 16kByte SRAM block
MP3 decoder code execution by core
Access to the MP3 data for decompression
Decompressed audio stream to 112kByte SRAM block
DMA transfer to audio output stage (I2S)
User interface: DMA transfers of the graphical icons from Flash to display
Notes: In addition to a performance equivalent to 0-wait execution from Flash using the ART Accelerator, the 32-bit multi-AHB bus matrix interconnects all masters (at the top of the chart: CPU, DMAs, Ethernet, USB HS) and slaves (on the right-hand side: Flash memory, SRAM, FSMC, AHB and APB peripherals) and ensures a seamless and efficient operation even when several high-speed peripherals are working simultaneously. The nodes on the matrix represent the actual connections over the 7-layer matrix, between master and slave.
For instance, let’s take the example of an MP3 audio player with graphical user interface. A compressed audio stream coming from the USB high speed peripheral is directly stored in the 16kB system RAM block thanks to the DMA controller dedicated to the USB high speed peripheral. In parallel, the CPU can process the audio data (MP3 decompression and/or equalizer) taking full advantage of the DSP extension of CM4. The processed data are written into the 112kB system RAM block and are transferred automatically with the system DMA controller to the I2S interface which transmit synchronously the audio data to an external CODEC. In parallel, the second system DMA controller can fetch graphical content from the flash to build automatically the Graphical User Interface on the external display connected to the STM32F4 through the FSMC interface.

## Slide 21: Outstanding power efficiency
  ART Accelerator™ reducing the number of accesses to Flash
  Voltage scaling to optimize performance/power consumption
VDD min down to 1.7 V
Low-power modes with backup SRAM and RTC support
Typical values in VBAT mode
230 μA/MHz, 38.6 mA at 168 MHz executing Coremark benchmark from Flash memory (with peripherals off), made possible with:
  ST’s 90 nm process allowing the CPU core to run at only 1.2 V
Notes: 230 µA/MHz, 38.6 mA at 168 MHz (executing Coremark benchmark from Flash memory, with ART Accelerator™ enabled and all peripherals off),
1.2 V is supplied by an internal regulator with power scaling support: the user can choose between 2 settings of the regulator (lower voltage for mid performance with 10% less dynamic consumption, higher voltage for high performance).
VDD min down to 1.7 V (on all packages except the LQFP64 which offers 1.8 V min)
Besides the LQFP64, all packages offer the option, through a dedicated pin, to turn off the brownout protection which is trimmed to reset the microcontroller below 1.8 V. When the brownout is disabled, the product can work down to 1.7 V min. This feature allows the product to be used in low-voltage applications where a 1.8 V regulator (+/- 5%) requires the microprocessor to work down to 1.7 V. Such applications usually provide a reset circuit that handles the reset management of the microcontroller.
Low power modes with backup and SRAM and RTC support. For instance, in Vbat mode, the RTC and backup SRAM typically draw less 1uA each

## Slide 22: Low power and real life applications
Run
Low power
% Low power mode
time
mA/MHz
%
Run
Mode
Run
Low power
Average consumption
time
mA/MHz
Low power in real life applications is not just Low-power mode
Need to consider the % of time spend in LP mode and in Run mode

## Slide 23: Average consumption
mA @100 MHz
20
40
50
30
10
0
20
40
60
80
100
% Run
Competitor F
Competitor R
If competitors are claiming better low-power modes, these are only an advantage if the overall system is spending more than 90% of the time doing nothing in low-power mode
STM32 F4

## Slide 24: STM32 F4 block diagram
Feature highlight
168 MHz Cortex-M4 CPU
  Floating point unit (FPU)
  ART Accelerator TM
  Multi-level AHB bus matrix
1-Mbyte Flash, 192-Kbyte SRAM
1.7 to 3.6 V supply
RTC: <1 µA typ, sub second accuracy
2x full duplex I²S
3x 12-bit ADC 0.41 µs/2.4 MSPS
168 MHz timers
Notes: 1.7 V on all packages except LQFP64 which offers 1.8 V VDDmin
3x 2.4 MSPS ADC (up to 7.2 MSPS in interleaved mode)

## Slide 25: STM32 F4 portfolio
Notes: 25
Scalable product offer
  - Get the right product from more than 30 derivatives
  Develop your platform or upgrade your application by taking a larger package or larger memory size or richer set of peripherals
All part numbers are in production except the WLCSP available in TBC.

## Slide 26: Extensive tools and SW
Evaluation board for full product feature evaluation
  Hardware evaluation platform for all interfaces
  Possible connection to all I/Os and all peripherals
Discovery kit for cost-effective evaluation and prototyping
Large choice of development IDE solutions from the STM32 and ARM ecosystem
STM32F4DISCOVERY $14.90
STM3240G-EVAL
$349

## Slide 27: Software Libraries
ST software libraries free at www.st.com/mcu
C source code for easy implementation of all STM32 peripherals in any application
  Standard library – source code for implementation of all standard peripherals. Code implemented in demos for STM32 evaluation board
  Motor Control library – Sensorless Vector Control for 3-phase brushless motors
ARM CMSIS DSP library – (free with license agreement)
Audio library – MP3/WMA decoder, volume control, equalizer
(free with license agreement).
ST engineered, tested, documented and free

## Slide 28: JPEG Demo
STM32F4
LCD
Cortex-M4 Core
Flash memory
SRAM
DMA
FSMC
Code
JPEG Images
Decoded pixel buffer
Data[0…15]
Addr[0…20]
Fetch code and Image block from Flash to Core
Decode JPEG block
Store decoded image block to SRAM pixel buffer
Continue above process until SRAM Pixel buffer full.
Set DMA.
DMA transfers pixel data from SRAM to LCD through FSMC without Core
Continue first process until whole image drawn
FPU
SRMA ->FSMC

## Slide 29: Thank you
www.st.com/stm32f4